## Slide 1: Effect of Bit-Level Correlation in Stochastic Computing
Megha Parhi, Marc D. Riedel, Keshab K. Parhi
Department of Electrical and Computer Engineering
University of Minnesota, Minneapolis MN, USA

## Slide 2: Outline
Introduction
Objective
Theoretical Results
Simulated Results
Conclusions and Future Work

## Slide 3: Stochastic Computing
Stochastic number can be represented in two formats, where each bit has the same weight.
  Unipolar: and
  Bipolar: and
Notes: 𝑋: stochastic bit stream

## Slide 4: Properties of Stochastic Computing
Stochastic Computing: A number is represented by a string of 1’s and 0’s. The percent of 1’s in the number represents the value of the number represented as a probability. It was proposed in 1967 by Gaines as an alternative to binary computing. Stochastic logic gates compute an approximation of the output as opposed to an exact value.
Applications: These are well suited in low-speed area-constrained applications such as biomedical applications, and cyber-physical systems operating at low rates.
Advantages:
  Low complexity in computing, small in size, low power
  Fault-tolerance due to redundancy
Disadvantages
  Long computation time (if bit stream is long)
  Low Accuracy (if bit stream is short)
  Multiplying by 2 and checking sign in bipolar are expensive operations

## Slide 5: Example of Stochastic Multiplication

## Slide 6: Outline
Introduction
Objective
Theoretical Results
Simulated Results
Conclusions and Future Work

## Slide 7: Previous Work
Parker and McCluskey discuss how to treat probability in a logic gate without using stochastic bit streams where multiple bit streams are uncorrelated at bit-level (1975).
Qian et al present approaches to synthesize a certain probability assuming that the bit streams are independent (2009, 2011).
Alaghi and Hayes use an approach that uses Stochastic Correlation and have proposed a method to generate correlated bit streams using probabilistic transfer matrices (2013).
Objective-1: Analyze output when multiple bit streams are correlated at the bit-level.
Objective-2: Generate correlated bit streams.

## Slide 8: Multi-Sensor Processing System
MIMO
System

## Slide 9: Bit-Level Correlation
This work presents a method to analyze effect of bit-level correlation and generate correlated bit streams using Pearson correlation for unipolar
Each bit is a Bernouli random variable. Sum of Bernouli is a Binomial RV, For long bit stream, binomial approximates a Gaussian RV

## Slide 10: Outline
Introduction
Previous Work
Objective
Theoretical Results
Simulated Results
Conclusions and Future Work

## Slide 11: Closed Form Expressions for Single Logic Gates
Gate Type | Independent | Correlated
AND |  | 
AND ( inverted) |  | 
NAND |  | 
OR |  | 
OR ( inverted) |  | 
NOR |  | 
XOR |  | 
XNOR |  | 
MUX ( select signal) |  | 
Gate Type | Independent | Correlated
AND |  | 
NAND |  | 
OR |  | 
NOR |  | 
XOR |  | 
XNOR |  | 

## Slide 12: Error Analysis
Gate Type | Error
AND | 
NAND | 
OR | 
NOR | 
XOR | 
XNOR | 
Gate Type | Error
AND | 
NAND | 
OR | 
NOR | 
XOR | 
XNOR | 

## Slide 13: Synthesis Correlated Bit Streams from Uncorrelated Bit Streams (Unipolar)
 |  |  | Marginal
Marginal |  |  | 
 |  |  | Marginal
Marginal |  |  | 
Let
Calculate:

## Slide 14: Synthesis of Two Correlated Stochastic Bit Streams
Input: , and .
Output: and .

## Slide 15: Synthesized Circuit using LFSR, MUX

## Slide 16: Range
Minimum Correlation Coefficient
Maximum Correlation Coefficient

## Slide 17: Constraints for Correlation

## Slide 18: Synthesis of Three Correlated Stochastic Bit Streams
Input: , and ; , , and .
Output: , and .

## Slide 19: Circuit Diagram of Synthesized Circuit

## Slide 20: Outline
Introduction
Previous Work
Objective
Theoretical Results
Simulated Results
Conclusions and Future Work

## Slide 21: Simulated Results

## Slide 22: Simulation Results of Stochastic Logic Given Correlated inputs

## Slide 23: Example using Logic Gates
=

## Slide 24: Conclusion
Presented an approach to analyze effect of bit-level correlation
Presented synthesis of correlated bit streams
Simulation results confirm results predicted from theory